20” Disk Sander for My Lathe

By: Raymond Lanham

Inspired Gary Smith in Michigan, I built this 20" disk sander for my  3520B PowerMatic "Mustard Mistress". It adjusts from 80 to 136 degrees.

Created from kitchen sink cut-out material (Formica /Laminex on one side), the triangle gussets are glued into dados in the base. The under supports for the table are glued into dados in the top. 1/4-20 tpi carriage bolts hold the top joints. The lower adjustable points are 5/16-18 tpi carriage bolts and the carriage bolt that holds it to the lathe is 3/8-20 tpi with a Rockler knob.

I filled the edges of the particle board with spackle and then sanded them smooth. Black paint was used to finish the edges and the over-brush marks were simply scraped off the Formica /Laminex  surfaces. Purple heart was used to edge the top. A 20" PSA, 80 grit disk was procured for $14

This shows how the disk is attached to the lathe. There is a 4" faceplate screwed to an 8" Particle board disk, glued to a 15" MDF disk, bolted to the 20" MDF disk with 1/4-.20 flat  head bolts and Nylok nuts.

The disk was then sealed with several coats of shellac in order to create a smooth surface for the PSA sandpaper to adhere.

The miter slot has been routed and the edge of the table beveled to 45 degrees to accommodate sanding close to the disk even when sanding at an angle.

The base was made wide enough for the support arms to clear the bed of the lathe when sanding at the most extreme position of the table adjustment.

Fine sandpaper was glued with contact cement to the underside of the base to provide gripping power when the knob is tightened.

20” Disk sander from Powermatic……………………….………..…$2,100.00

20” Disk sander from LaGuna Tools…………………………………..$795.00

Building it myself for less then $20.00……………………………….Priceless!